## Slide 1: USPAS – Simulation of Beam and Plasma Systems Steven M. Lund, Jean-Luc Vay, Remi Lehe, Daniel Winklehner and David L. Bruhwiler
U.S. Particle Accelerator School sponsored by Old Dominion University
http://uspas.fnal.gov/programs/2018/odu/courses/beam-plasma-systems.shtml
January 15-26, 2018 – Hampton, Virginia
Instructor: David L. Bruhwiler
Contributors: G. Andonian, UCLA / RadiaBeam Tech
G. Andonian, UCLA / RadiaBeam Tech
This material is based upon work supported by the U.S. Department of Energy, Office of Science, Offices of High Energy Physics and Basic Energy Sciences, under Award Number(s) DE-SC0011237 and DE-SC0011340.
Lecture: Slice Energy Spread

## Slide 2: Goals
TBD

## Slide 3: High-quality electron beams (high charge, short duration, low emittance) can drive Free Electron Laser
https://www.helmholtz-berlin.de/projects/berlinpro/erl-intro/linac-fel_en.html
Gain length
Free Electron Laser:
Interaction undulator radiation & dense e-beam  micro-bunching  coherent undulator emission
Small gain length favorable
E-beam quality  Pierce parameter ρ
Large ρ favorable (ρ typically of order 10-3-10-2)
Energy spread washes out micro-bunching
1D gain length corrected with 3D effects Λ (energy spread, emittance, etc.)
Huang & Kim PRSTAB 10, 034801 (2007)
Pierce parameter
Charge / duration
E-beam energy
E-beam size (emittance)
3D Gain length
This slide courtesy of J. van Tilborg (LBL)

## Slide 4: Each time slice can develop micro-bunching: Not integrated but slice energy spread critical to FEL: σγ,slice<ρ
3D Gain Length as a function of energy spread in a correlation-free beam:
z
γ
σγ
z
γ
σz0
σγ
D×σz0
Instantaneous energy spread of slice: σγ/D
Adding correlation through chicane de-compression:
Beam parameters:
5 pC in 10 fs
250 MeV
Emittance 0.5 μm
Beam size 25 μm
Undulator:
Period 2.18 cm
Strength K=1.26
Pierce ρ=0.007
De-compression D>1
D=1
1D Gain Length
No correlation
Same beam, with correlation
3D Gain Length
Slippage of chirped e-beam through photon pulse is detrimental
Length of relevant slice is several radiation wavelengths long (~5 fs)
Chicane de-compression:
Maier et al. PRX 2012, Schroeder et al. FEL2013
This slide courtesy of J. van Tilborg (LBL)

## Slide 5: Bunch length and energy spread known, but correlation not known (longitudinal phase phase not known)
Bunch duration: 5 pC in 10 fs
Correlation unknown
Chicane scan
This slide courtesy of J. van Tilborg (LBL)

## Slide 6: Class discussion:
Any questions at this point?
Have

## Slide 7: The accelerator design workflow

## Slide 8: Wrap up
Any final questions regarding the material in this lecture?
Have